## Slide 1: Solutions for low alcohol beer
CEBC - 2021

## Slide 2: Low or no alcohol beer – common criticisms
Beers are overly sweet
Beers are worty
Beers are thin and lack mouthfeel
How do we over come these criticisms to create a drinkable beer?

## Slide 3
Creating a great tasting low or no alcohol beer requires a holistic approach to both wort and beer creation. All parts make up the whole and must be considered when designing low alcohol beers.
Great tasting low or no alcohol beer
Wort Production and design
Fermentation Method
Choice of Organism
Alcohol removal or dilution
pH correction
Stabilisation

## Slide 4
Understand the importance of wort composition in recipe design
% of normal wort sugars
10-15
50-60
15-20
20-30
Glucose DP1
Maltose DP2
Maltotriose DP3
Dextrin DP4+
+
Notes: Under normal circumstances brewers wort is made up of anywhere between 75% and 95% fermentable sugar. Yeast in the presence of fermentable sugar creates alcohol. In order to create less alcohol we need either reduce the concentration of fermentable sugars in the wort, use a yeast unable to consume all the sugars, or a combination of the two techniques

## Slide 5
More of this
Less of this
CH3CH2OH
Understand mash enzymes and modify your fermentability
beta amylase
alpha amylase
fermentability
Key
76-820C
Temperature
brewers window
low alc window
64-700C
Enzyme activity
=
Notes: The mashing process relies on two enzymes, beta amylase and alpha amylase. A normal mash aims to maximise starch breakdown by activating both enzymes near their optimum temperature, the so called brewers window. The fermentability of wort can be skewed in favour of being less fermentable by mashing in at higher temperatures to avoid beta amylase activity this is the low alcohol window.

## Slide 6: Some experimental work with high mashing technique

## Slide 7: Mash temperature Trials
Idea is to inactivate beta amylase while keeping alpha amylase active
5 different single mash temperatures
Four time periods
7.5 Plato wort
Notes: Formed the basis of an experiment.

## Slide 8: AB Vickers Trials (mash bath + iodine)
 |  | Mash Temperature 0C |  |  |  | 
 |  | 74 | 78 | 82 | 86 | 95
Mash Time (min) | 60 | S1 | S5 | S9 | S13 | S17
 | 70 | S2 | S6 | S10 | S14 | S18
 | 80 | S3 | S7 | S11 | S15 | S19
 | 90 | S4 | S8 | S12 | S16 | S20
Initial mashing regime
Iodine test
74
78
82
86
95
60
70
80
90
Notes: The initial experimental procedure. Amylopectin and starch will stain black with iodine while dextrin and erythrodextrin material will stain red

## Slide 9: Mascoma analysis (size exclusion chromatography)
74
78
82
86
95
g/100ml
Good potential
Too much starch + some fermentable sugar
Possibly too much starch
Good potential
Too much fermentable sugar
Notes: Wort strength 1.020
Further work by Mascoma using SEC chromatography gave good data. Heat map produced shows which temperatures produced the most dextrin and least fermentable sugars

## Slide 10: Project Status: Montreal / Mascoma analysis
Notes: More in depth data shows how the degree of polymerisation is influenced by temperature. Of most interest is DP 4-7

## Slide 11: Other wort production considerations
Malt bill
Wort strength
Hopping rates
Boil times and additions
Liquor salts

## Slide 12
Creating a great tasting low or no alcohol beer requires a holistic approach to both wort and beer creation. All parts make up the whole and must be considered when designing low alcohol beers.
Great tasting low or no alcohol beer
Wort Production and design
Fermentation Method
Choice of Organism
Alcohol removal or dilution
pH correction
Stabilisation

## Slide 13
Choose you micro-organism(s). Understand and control the flow of carbon from sugar to metabolite
Organism
Alcohol
Lactic acid
Ferments
Produces
Ale
Lalbrew London / Windsor
Maltose negative
Acid producing
Lactic acid bacteria
X
X
X
X
X
X
X
X
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
✔
X
✔
✔
Notes: The final ethanol content of a beer can be influenced by the yeast and bacteria chosen for fermentation. Some yeast will only ferment simple sugars, naturally reducing the final ethanol content while others will ferment glucose to lactic acid instead of ethanol. Understanding the properties of the organism you choose can help influence the final ethanol content of the beer and control the pH.

## Slide 14: Fermentation options
Standard fermentation with a maltose negative yeast
Kettle or FV souring with bacteria followed by fermentation with maltose negative yeast
Standard fermentation with maltotriose negative yeast and hot mashing
Kettle or FV souring with bacteria followed by fermentation with maltotriose negative yeast along with hot mashing
Cold contact fermentation (lager yeast)

## Slide 15
Creating a great tasting low or no alcohol beer requires a holistic approach to both wort and beer creation. All parts make up the whole and must be considered when designing low alcohol beers.
Great tasting low or no alcohol beer
Wort Production and design
Fermentation Method
Choice of Organism
Alcohol removal or dilution
pH correction
Stabilisation

## Slide 16: Alcohol removal or dilution
Sometimes even using hot mashing and yeasts of limited fermentability a dilution step is required to meet the desired alcohol step. Ideally this should be made with sterile deaerated water.
For very low alcohol content an alcohol removal step may be required. There are many technologies out there but reverse osmosis (RO) seems to be the technique being favoured

## Slide 17
Creating a great tasting low or no alcohol beer requires a holistic approach to both wort and beer creation. All parts make up the whole and must be considered when designing low alcohol beers.
Great tasting low or no alcohol beer
Wort Production and design
Fermentation Method
Choice of Organism
Alcohol removal or dilution
pH correction
Stabilisation

## Slide 18: The Importance of pH correction
Problems:
Low gravity worts can lead to high pH due to their limited buffering capacity
Limited fermentation compounds the issue as yeast produce organic acids during fermentation
This can lead to:
Astringent tannic worts
A high degree of perceived bitterness
Poor microbiological stability including the potential for growth of pathogens

## Slide 19: The Importance of pH correction
Solutions:
Correct pH at all stages, mash, boil, post boil and post fermentation using food grade acid additions
Hop at an appropriate level
Adjust the pH of sparge water to the desired wort pH (5-5.2) by acid addition to the HLT
An additional point here is that it is possible to use many different acids at this point and each will impart a different flavour

## Slide 20
Creating a great tasting low or no alcohol beer requires a holistic approach to both wort and beer creation. All parts make up the whole and must be considered when designing low alcohol beers.
Great tasting low or no alcohol beer
Wort Production and design
Fermentation Method
Choice of Organism
Alcohol removal or dilution
pH correction
Stabilisation

## Slide 21: Stabilisation
Stabilisation is the most commonly overlooked factor in the production of low alcohol beers by craft brewers. If we think about regular beer it is relatively microbiologically stable and pathogens struggle to grow or survive for the following reasons.
It is nutritionally poor / depleted
It has a high alcohol content
It has a low pH
It contains hop acids
All of these are altered or reduced to a degree in low alcohol beer

## Slide 22: How to stabilise
It can be a dirty word among craft brewers but the gold standard way of stabilising beer is to pasteurise after packaging using a tunnel pasteuriser.
Flash pasteurisation has a lower footprint and is easier to implement but there is risk to the product from contamination during the brewing process
Chemical stabilisation using Potassium Sorbate or Sulphur Dioxide

## Slide 23: Conclusions
Making low alcohol beer isn’t as simple as adding a different yeast to one of your regular beers. It requires a holistic approach taking into account all parts of the whole and some serious R&D effort to get it right.
As a first step I would recommend the following:
High temperature mashing
Fermentation with maltotriose negative yeasts (London or Windsor)
pH correction
Stabilisation

## Slide 24: Questions